## Slide 1
UNITREE G1 / SDK WRAPPER V3
A hardware-facing Python adapter
A guided tour of 1,388 lines: DDS, motion, arms, hands, audio, SLAM, sensing, and IK
G1(...) → stable Python API → live robot / simulation
Based on static source analysis • no robot commands executed

## Slide 2
ORIENTATION
What this file is
A compatibility-and-convenience layer around Unitree SDK2 and several external robot interfaces
STATIC EXPLANATION • SOURCE: g1/dev/sdk_wrapper_v3.py
02
One public object
`G1` owns clients, subscriptions, cached state, and action methods.
Callers do not need to construct DDS publishers or decode messages.
Lines 517–1388
Many transports
Unitree RPC / DDS
ZeroMQ RGB-D
TCP Modbus/TCP
Piper subprocess + audio RPC
Lazy-loaded FK/IK
The wrapper is an adapter, not a simulator.
Observable contract
Returns dicts, tuples, status codes, raw messages, and errors.
It favors best-effort compatibility across SDK message layouts.
Hardware-side effects are real for motion methods.

## Slide 3
MENTAL MODEL
System architecture
The wrapper sits between application code and several live data/control planes
STATIC EXPLANATION • SOURCE: g1/dev/sdk_wrapper_v3.py
03
Application
Dashboard • script • ROS node
G1 API
State • motion • sensing • actions
Robot / services
DDS • RPC • network
DDS topics
rt/lowstate
rt/odommodestate
rt/audio_msg
rt/dex3/*
rt/unitree/slam_*
SDK clients
LocoClient
MotionSwitcherClient
AudioClient
G1ArmActionClient
RobotStateClient / SLAM RPC
External interfaces
ZeroMQ camera stream
Modbus/TCP Inspire hands
Piper TTS binary + models
ArmFK / ArmIK

## Slide 4
LINES 1–24
Imports and dependency boundaries
Most behavior is delegated to Unitree SDK2; local code normalizes and orchestrates it
STATIC EXPLANATION • SOURCE: g1/dev/sdk_wrapper_v3.py
04
Python standard library
audioop / wave
importlib / pathlib
json / math / re
socket / struct
subprocess / tempfile
threading / time
Unitree SDK2
ChannelFactoryInitialize
ChannelPublisher / Subscriber
LocoClient
MotionSwitcherClient
AudioClient
G1ArmActionClient
RPC Client + CRC
IDL message types
Optional / dynamic
numpy — matrices, clipping, IK
arm_fk / arm_ik — imported inside a guarded try
RobotState / Video clients — importlib fallback
zmq — imported only by get_rgbd()
Piper — external executable + voice model

## Slide 5
LINES 26–107
Constants define the robot contract
The wrapper encodes joint indexing, action names, hand limits, network endpoints, and topic discovery
STATIC EXPLANATION • SOURCE: g1/dev/sdk_wrapper_v3.py
05
Modes & actions
FSM_IDS:
zero_torque=0 • damp=1
prepare=4 • walk=501
run=802
HL_ARM_ACTIONS maps human labels to action IDs 11–99.
Aliases make CLI/UI text forgiving.
29 body joints
0–5 left leg | 6–11 right leg
12–14 waist
15–21 left arm
22–28 right arm
LOWCMD_JOINTS = all groups
UPPER_BODY_JOINTS = waist + arms
Dex3 hands
7 named joints per hand
HAND_MIN / HAND_MAX clamp targets
HAND_OPEN / HAND_CLOSED poses
rt/dex3/{left,right}/cmd + /state
Other constants
BMS_TOPICS: four candidate battery topics
INSPIRE_CONFIGS: .210 right / .211 left, port 6000
INSPIRE_OPEN / CLOSE: six Modbus values
SLAM_POINT_TOPICS: four point-cloud topics
_PIPER_VOICES: en/de/fr/es/ar model aliases
Named RGB colors + #RRGGBB + R,G,B

## Slide 6
LINES 552–578
Topic map: what is subscribed at startup
G1 subscribes eagerly to a set of “latest value” streams
STATIC EXPLANATION • SOURCE: g1/dev/sdk_wrapper_v3.py
06
Core state
rt/lowstate
rt/odommodestate
rt/sportmodestate
rt/odom
rt/unitree/slam_mapping/odom
Perception & diagnostics
rt/slam_info
rt/slam_key_info
rt/audio_msg
PointCloud2 on four SLAM topics
BMS topics × available message types
The _Latest pattern
Each subscription stores:
• most recent message
• wall-clock timestamp
get() returns (msg, ts).
Consumers can choose the freshest compatible stream and reject stale battery data.

## Slide 7
LINES 517–578
Startup lifecycle: constructing G1
Construction initializes DDS and subscriptions, while most command clients remain lazy
STATIC EXPLANATION • SOURCE: g1/dev/sdk_wrapper_v3.py
07
1
G1(iface, domain_id)
2
_ensure_factory()
3
LocoClient + Init()
4
Subscribe to state
5
Lazy clients = None
Important consequence
A G1 instance immediately opens DDS subscriptions. It may fail before any explicit action if the interface, SDK, message types, or robot-side DDS environment are unavailable.

## Slide 8
LINES 110–117, 592–642
Factory and lazy-client discipline
The wrapper protects global DDS initialization and caches SDK clients per G1 instance
STATIC EXPLANATION • SOURCE: g1/dev/sdk_wrapper_v3.py
08
_ensure_factory(domain_id, iface)
cfg = (int(domain_id), str(iface))
First call:
ChannelFactoryInitialize(domain, iface)
Later call with same cfg:
allowed
Later call with different cfg:
RuntimeError
Lazy accessors
_motion_client()
_audio_client()
_arm_action_client()
_video_client()
_slam_client()
_lowcmd_client()
_arm_sdk_client()
_dex3_hand(side)
Each creates, configures, initializes, and caches exactly once.

## Slide 9
LINES 584–621, 165–199
Compatibility strategy: dynamic imports and tolerant reads
The code is designed to survive SDK/message-layout variation across Unitree robot families
STATIC EXPLANATION • SOURCE: g1/dev/sdk_wrapper_v3.py
09
_load_type()
Try primary module.
If the requested type is missing, try fallback module.
Else raise RuntimeError.
Used for LowState_.
importlib fallbacks
RobotStateClient:
b2 → go2
VideoClient:
g1 → go2
This keeps the wrapper usable with multiple SDK layouts.
_read(obj, name)
Missing attribute → default.
Callable attribute → call it.
TypeError during call → return callable itself.
The trade-off: fewer hard crashes, but weaker type guarantees.

## Slide 10
LINES 128–162
Input normalization helpers
Small helpers turn human/UI input into constrained SDK-ready values
STATIC EXPLANATION • SOURCE: g1/dev/sdk_wrapper_v3.py
10
_normalize_action()
lowercase
replace underscores with spaces
collapse whitespace
resolve aliases
“xray” → “x-ray”
“release” → “release arm”
_normalize_side() + _clamp_hand()
Accepts left / l / right / r.
Rejects anything else.
Each hand target is clamped component-by-component against HAND_MIN/MAX.
Color pipeline
_parse_color:
name → RGB tuple
#RRGGBB → RGB tuple
R,G,B → RGB tuple
reject invalid input
_scale_color:
intensity 0–100 → linear RGB scaling

## Slide 11
LINES 120–225
Parsing and small data adapters
These helpers normalize RPC responses, message objects, poses, vectors, and joint limits
STATIC EXPLANATION • SOURCE: g1/dev/sdk_wrapper_v3.py
11
_rpc_get_int()
Calls private Client._Call(api_id, "{}")
Requires code == 0 and data.
JSON → data → int.
Failure → None.
Used for FSM id / mode.
_mode_name / _vector3
_mode_name finds first non-empty name, mode, or alias.
_vector3 safely converts the first three values to floats.
Both return empty/None instead of raising on malformed data.
_clamp_arm_q()
If JOINT_LIMITS unavailable:
return q unchanged.
Otherwise:
build lower/upper arrays
np.clip(q, lo, hi)
The ArmIK path relies on this.

## Slide 12
LINES 202–328
Pose math: rotations and SLAM pose parsing
The wrapper uses NumPy 3×3 rotations and converts SLAM quaternion payloads into x, y, yaw
STATIC EXPLANATION • SOURCE: g1/dev/sdk_wrapper_v3.py
12
_rot_x / _rot_y / _rot_z
Each returns a float64 3×3 rotation matrix.
_ROT_BY_AXIS = (Rx, Ry, Rz)
ik_move_ee left-multiplies selected rotations onto the current end-effector frame.
_parse_slam_pose()
JSON decode.
Require dict + errorCode == 0.
Read currentPose x/y/z.
Quaternion → yaw, or use yaw.
Reject an all-zero pose.
Returns (x, y, yaw).
Quaternion yaw
yaw = atan2(
2(qw·qz + qx·qy),
1 − 2(qy² + qz²)
)
This intentionally keeps only planar heading for navigation.

## Slide 13
LINES 228–297
The DLS position solver
Position-only arm motion holds wrist joints fixed and solves shoulder/elbow with damped least squares
STATIC EXPLANATION • SOURCE: g1/dev/sdk_wrapper_v3.py
13
Inputs
ArmFK solver
side
target_T (4×4 pose)
q_init (7 arm joints)
optional selected_axis
Active joints = 0,1,2,3
Iteration
1. Compute current FK.
2. position error = target − current.
3. Finite-difference J (3×4).
4. Solve Jᵀ(JJᵀ+λ²I)⁻¹e.
5. Limit Δq norm to 0.3.
6. Clamp joint limits.
7. Restore q[4:] from q_init.
Success rules
Immediate success:
‖e‖ < 0.005 m.
After 64 iterations:
selected axis error < 0.006 m
and total error < 0.040 m
→ pos_axis_clamped
Else → None + diagnostics.

## Slide 14
LINES 331–485
Private support classes
Five small classes hide recurring DDS publishing, latest-value storage, threading, and RPC details
STATIC EXPLANATION • SOURCE: g1/dev/sdk_wrapper_v3.py
14
_Latest
Subscriber + callback.
Stores msg and timestamp.
get() → (msg, ts).
Used for every telemetry stream.
_HeadlightThread
Daemon = False.
Repeats LedControl(rgb) until duration.
Stop event interrupts waits.
Non-zero code stops loop.
Finally sends RGB (0,0,0).
set_headlight owns lifecycle.
_Dex3 / _LowCmd / _ArmSdk
Dex3: 7-joint hand commands + sensor snapshots.
LowCmd: rt/lowcmd, 29 joints, CRC.
ArmSdk: rt/arm_sdk, sparse targets, weight at motor 29.
All publish SDK message objects, not plain Python arrays.

## Slide 15
LINES 373–457
Low-level command paths
There are two body-command publishers plus a separate Dex3 hand publisher
STATIC EXPLANATION • SOURCE: g1/dev/sdk_wrapper_v3.py
15
rt/lowcmd
_LowCmd.write(q, mode_machine, ...)
Writes all 29 body joints.
Default kp/kd arrays.
Sets mode = 1.
Computes CRC before Write().
Used by move_ll_joint(..., arm_sdk=False).
rt/arm_sdk
_ArmSdk.write(targets, weight, ...)
Writes only supplied joint IDs.
Optional waist-specific gains.
motor_cmd[29].q = weight.
CRC before Write().
Used for upper-body ramps and IK.
rt/dex3/*/cmd
_Dex3._write(targets)
7 target positions.
mode = (i & 0x0F) | (1 << 4)
q, dq, tau, kp, kd.
move() repeats writes at a configured rate for hold_s.

## Slide 16
LINES 460–514
SLAM RPC and Inspire Modbus
Two network protocols sit beside DDS: JSON RPC for SLAM and binary Modbus/TCP for Inspire hands
STATIC EXPLANATION • SOURCE: g1/dev/sdk_wrapper_v3.py
16
_SlamClient
Client("slam_operate", False)
Registers APIs 1801, 1802, 1804, 1102, 1901.
Version = 1.0.0.1.
start_mapping → 1801
stop_mapping → 1802 or 1901
init_pose → 1804
pose_nav → 1102
All payloads are JSON with data.
_modbus_move()
Connect host:port with timeout.
Build MBAP header + PDU.
Function 6: select/control register.
Function 16: write six registers.
Preset 1522 and 1498 to 200.
Write values to 1486.
Raise on exception response.
Always close socket.
Addresses are hard-coded per robot setup.

## Slide 17
LINES 517–642
G1 object: one stateful façade
The constructor establishes shared resources; methods then expose capability-specific operations
STATIC EXPLANATION • SOURCE: g1/dev/sdk_wrapper_v3.py
17
Cached state
_path_points
_last_slam_pose
_initial_slam_pose
_gait_override
_slam_map_path
_headlight_thread
_dex3
_arm_fk / _arm_ik
Cached clients
_client = LocoClient()
motion / robot_state / audio
arm_action / video / slam
lowcmd / arm_sdk
All are initialized only when the corresponding feature is used.
Telemetry subscriptions
lowstate
sport + sport_alt
odom + slam odom
clouds + slam info/key
audio message
BMS topic/type combinations
The wrapper owns the latest message cache, not history.

## Slide 18
LINES 642–1388
Public API map: 72 methods in groups
The method surface is broad, but the responsibilities cluster cleanly
STATIC EXPLANATION • SOURCE: g1/dev/sdk_wrapper_v3.py
18
Status & modes
get_state
get_service
toggle_service
zero/damp/prepare/walk/run
toggle_dev_mode
get_gait / toggle_gait
get_lowstate
Motion & sensing
loco_move / loco_stop
get_odom / get_imus / get_battery
get_rgbd / get_point_cloud
get_slam_info / get_mic_input
move_ll_joint
say / set_headlight
Arms, hands & navigation
release/engage_arms
open/close Dex3 + sensors
open/close Inspire + sensors
start/stop mapping / relocate
add_map_pose / navigate
gesture actions
ik_move_ee / extend_arm
teach / repeat (not implemented)

## Slide 19
LINES 725–789
State and service management
get_state composes a dashboard-ready snapshot from several lower-level APIs
STATIC EXPLANATION • SOURCE: g1/dev/sdk_wrapper_v3.py
19
get_state()
Returns:
id / mode from private RPC calls
motion_mode + motion_code
gait
battery
lowstate
services
slam_info
This is a fan-out call: one failure from a nested method can fail the whole snapshot.
get_service() / toggle_service()
Service catalog: ai_sport, basic_service, g1_arm_example, vui_service, unitree_slam.
get_service:
SDK ServiceList if available; otherwise catalog rows with unknown status.
toggle_service:
status != 0 → enabled=True, then ServiceSwitch(name, enabled).
Returns previous status, requested enabled state, code.

## Slide 20
LINES 790–858
FSM modes and gait control
These methods issue motion-control RPCs and use fallback strategies when SDK methods differ
STATIC EXPLANATION • SOURCE: g1/dev/sdk_wrapper_v3.py
20
Direct FSM methods
zero_torque_mode() → SetFsmId(0)
damp_mode() → SetFsmId(1)
prepare_mode() → SetFsmId(4)
walk_mode() → SetFsmId(501)
run_mode() → SetFsmId(802)
get_gait()
Prefer sport message fields:
gait_type, gaitType, gait.
If SDK reports 0 but a local override exists, return override.
No message → override or None.
toggle_gait()
Enable: try SetBalanceMode(1), then SetGaitType(1).
Disable: try BalanceStand(0), setters(0), SetFsmId(walk).
Returns codes from attempts.
Override updates only after success.

## Slide 21
LINES 859–1010
Lowstate, odometry, IMU, and battery
Telemetry methods prefer the freshest/most compatible source and preserve raw SDK messages where useful
STATIC EXPLANATION • SOURCE: g1/dev/sdk_wrapper_v3.py
21
get_lowstate()
29+ motor positions q
velocities dq
estimated torques tau_est
IMU rpy / gyro / acc
raw message
None until rt/lowstate arrives.
get_odom() / get_imus()
Odometry preference:
sport state → rt/odom → SLAM odom.
get_imus accepts lowstate or sport:
rpy, gyro, acc, quaternion, temp.
Malformed fields become None rather than stopping telemetry.
get_battery()
Scan BMS topic/type pairs.
Accept only messages ≤3 s old.
Return BMS fields if found.
Fallback to LowState:
power_v / power_a / bit_flag
battery_timeout = bit 0x10
BMS subset

## Slide 22
LINES 908–932, 1008–1027
Locomotion and arm handoff
Motion calls are deliberately bounded; arm control uses smooth weight ramps to hand off ownership
STATIC EXPLANATION • SOURCE: g1/dev/sdk_wrapper_v3.py
22
loco_move(vx, vy, vyaw, duration)
Move(..., continous_move=True)
Sleep for duration.
finally: loco_stop().
Returns the initial SDK code.
A typo in the SDK keyword “continous_move” is preserved.
loco_stop()
Prefer StopMove().
Fallback: Move(0,0,0, continous_move=False).
Use this as the safety stop for timed locomotion.
release / engage arms
Read current upper-body pose.
Publish through rt/arm_sdk.
Release: 151 frames, weight 1→0.
Engage: 51 frames, weight 0→1.
Smoothstep ramp:
r²(3−2r)
Waist gains are stronger.

## Slide 23
LINES 885–907, 933–1007
Audio output and headlight control
Audio combines local TTS conversion with robot audio playback; lighting uses a timed background thread
STATIC EXPLANATION • SOURCE: g1/dev/sdk_wrapper_v3.py
23
say(text, language, volume)
Find Piper from env or PATH.
Resolve language alias to model name.
Require ~/.local/share/piper/...onnx.
Generate temporary WAV.
Convert stereo → mono.
Convert sample width → 16-bit.
Resample → 16 kHz.
Set robot volume + PlayStream().
Returns audio RPC code.
set_headlight(color, intensity, duration)
Parse and scale RGB.
Stop and join previous light thread.
Immediate LedControl(rgb).
If duration > 0, start _HeadlightThread.
Thread repeats every 0.2 s.
On exit: LedControl(0,0,0).
Potential blocking point: join() waits for the previous thread to finish.

## Slide 24
LINES 1012–1077
Camera and point-cloud paths
Vision data is decoded from a local ZeroMQ stream or from DDS PointCloud2 messages
STATIC EXPLANATION • SOURCE: g1/dev/sdk_wrapper_v3.py
24
get_rgbd()
Try endpoints in order:
tcp://0.0.0.0:5555
tcp://127.0.0.1:5555
tcp://localhost:5555
SUB socket receives multipart:
RGB JPEG • depth PNG • scale.
Reject packets with <3 parts.
Last exception is re-raised.
get_point_cloud()
Choose newest of four cloud topics.
Map fields x/y/z to offsets.
Compute point count from width × height.
Downsample to at most 20,000 points.
Unpack little-endian float32.
Discard non-finite values.
Returns list of {x,y,z} dicts; empty list on malformed message.

## Slide 25
LINES 1110–1150, 373–410
Dex3 hand API
Dex3 is a DDS position controller with sensor snapshots and graceful per-hand error results
STATIC EXPLANATION • SOURCE: g1/dev/sdk_wrapper_v3.py
25
open / close
hand = left, right, or both
Move fixed HAND_OPEN/CLOSED pose
Default hold = 0.6 s
Default rate = 50 Hz
Both returns a dict by side.
One side returns one result.
get_dex3_hand_sensors()
Snapshot latest HandState_.
Positions q
Velocities dq
Estimated torques tau_est
Tactile pressures
Tactile temperatures
Lost flags
No state → “hand not detected”.
Error contract
_hand_error returns:
{hand, ok: False, action, error}
Exceptions are caught per side.
One faulty hand does not hide the other hand result.
This is useful for dashboards.

## Slide 26
LINES 1152–1192
Inspire hand API
Inspire controls are isolated behind fixed IPs and a small Modbus/TCP register sequence
STATIC EXPLANATION • SOURCE: g1/dev/sdk_wrapper_v3.py
26
Configuration
right → 192.168.123.210
left → 192.168.123.211
port = 6000
unit_id = 1
Six-register OPEN and CLOSE arrays are constants.
open / close flow
Normalize sides.
For each side:
lookup host/port/unit
call _modbus_move(values)
return success or _hand_error
Default hand = both.
Sensors
get_inspire_hand_sensors()
always returns “hand not detected”.
It is an explicit stub, not a transport implementation.
teach() and repeat() are also explicitly unimplemented.

## Slide 27
LINES 1194–1246
SLAM lifecycle and path queue
Navigation is stateful: poses are remembered, queued, and then sent one by one
STATIC EXPLANATION • SOURCE: g1/dev/sdk_wrapper_v3.py
27
start_mapping()
save current pose
call API 1801
add_map_pose()
capture current
(x,y,yaw)
navigate()
send queued poses
API 1102
stop_mapping()
call API 1802
or 1901
relocate()
Uses current pose, last pose, initial pose, or (0,0,0); calls API 1804 with G1_SLAM_MAP_PATH (default /home/unitree/test.pcd). On success, updates the cached poses.

## Slide 28
LINES 1248–1271
Microphone input and expressive gestures
The wrapper exposes audio messages as polling results and maps friendly gesture names to SDK action IDs
STATIC EXPLANATION • SOURCE: g1/dev/sdk_wrapper_v3.py
28
get_mic_input(duration_s, poll_s)
Poll latest rt/audio_msg.
Deduplicate by timestamp + raw text.
Try JSON decode.
Return timestamp, topic, raw, payload, text.
duration_s ≤ 0 → one immediate read.
duration_s > 0 → poll until deadline.
Gesture methods
clap() → “clap”
face_wave() → “face wave”
high_wave() → “high wave”
shake_hand() → action + release after 2 s
hug() → action + release after 2 s
left_kiss() → “left kiss”
_exec_arm_action accepts label or ID.

## Slide 29
LINES 1079–1108
Single-joint low-level motion
move_ll_joint chooses between the arm SDK handoff path and the full-body lowcmd path
STATIC EXPLANATION • SOURCE: g1/dev/sdk_wrapper_v3.py
29
arm_sdk=True (default)
Valid IDs: 12–28 only.
Read current upper-body pose.
Replace one joint target.
Publish sparse pose on rt/arm_sdk.
Waist gains: kp 480 / kd 12.
Returns {joint_id, arm_sdk: True}.
arm_sdk=False
Valid IDs: 0–28.
Wait for current q + mode_machine.
Replace one q in 29-joint vector.
Override kp/kd for selected joint.
Publish all joints to rt/lowcmd.
CRC applied by _LowCmd.
Returns topic = rt/lowcmd.

## Slide 30
LINES 1273–1369
IK architecture: from pose increment to motor frames
ik_move_ee separates geometry, solving, limits, rate limiting, and command streaming
STATIC EXPLANATION • SOURCE: g1/dev/sdk_wrapper_v3.py
30
1. Input
hand
delta_q / pose_increment
max_speed
max_dq
rate_hz
position_only
2. Target
current upper-body q
FK(q_init)
add dx/dy/dz
optional Rx/Ry/Rz
left-side sign rules
3. Solve
position-only DLS
or ArmIK DLS
joint limits
success diagnostics
None on failure
4. Shape
clip Δq to max_dq
step limit = speed/rate
smoothstep ramp
final joint target
5. Write
rt/arm_sdk
kp/kd
sleep 1/rate
return pose + steps

## Slide 31
LINES 1273–1369
ik_move_ee: detailed behavior and side conventions
The same API supports 3D translations, 6D increments, full IK, and a safer position-only mode
STATIC EXPLANATION • SOURCE: g1/dev/sdk_wrapper_v3.py
31
Input normalization
delta_q is an alias for pose_increment.
3 values → append 3 zeros.
6 values expected:
[dx, dy, dz, droll, dpitch, dyaw].
Anything else raises ValueError.
Left-hand signs
Translation:
target y += dy for right
target y -= dy for left
Rotation:
roll and yaw invert for left
pitch always uses -dpitch
This encodes mirror symmetry.
Streaming
Δq = q_sol − q_init.
Clip each joint delta to max_dq.
Compute number of frames from max joint move.
Use smoothstep interpolation.
Publish at rate_hz.
Returns joint_targets, ee_pose, ik info, steps.

## Slide 32
LINES 1371–1384
extend_arm: repeated position-only motion
extend_arm is a convenience loop that decomposes one displacement into small DLS moves
STATIC EXPLANATION • SOURCE: g1/dev/sdk_wrapper_v3.py
32
Inputs
hand
dx / dy / dz
steps (minimum 1)
max_speed
max_dq
rate_hz
Decomposition
step_increment = [dx/n, dy/n, dz/n, 0,0,0]
For each step:
call ik_move_ee(..., position_only=True)
collect result
Return
{hand, steps, step_increment,
position_only: True, results}
It does not stop early on a failed sub-step; callers must inspect each result.

## Slide 33
CROSS-CUTTING
Return values and error philosophy
The wrapper mixes SDK codes with structured Python results; consumers should inspect both
STATIC EXPLANATION • SOURCE: g1/dev/sdk_wrapper_v3.py
33
Raw-ish returns
Mode setters → SDK code
loco_stop → SDK return
say / set_headlight → int code
gesture methods → action code
start/stop mapping → {code, raw}
Structured returns
get_state dict
get_lowstate dict
get_battery dict
hand operation dicts
IK diagnostics + targets
navigation list of targets/codes
Exceptions
Invalid user input → ValueError
missing dependencies → RuntimeError
timeout → TimeoutError
missing files → FileNotFoundError
network failures → propagated or wrapped per method
No global exception policy.

## Slide 34
READ BEFORE RUNNING
Safety and operational caveats
This is control code: static understanding is not a substitute for robot-side validation
STATIC EXPLANATION • SOURCE: g1/dev/sdk_wrapper_v3.py
34
Motion side effects
FSM setters change robot mode.
loco_move drives for duration.
lowcmd / arm_sdk publish torque/gain commands.
Hand methods move physical fingers.
IK writes arm commands at 50 Hz by default.
Environment assumptions
DDS NIC defaults are supplied by caller.
Hard-coded Inspire IPs.
Hard-coded SLAM map fallback path.
Piper binary + model must exist.
ZMQ camera server must be reachable.
SDK message layouts must match.
Recommended checks
Use simulation or lifted robot first.
Verify iface/domain and service state.
Test telemetry-only methods.
Set conservative speeds/gains.
Keep an independent E-stop.
Inspect return codes and nested results.
Do not assume “success” means contact-free motion.

## Slide 35
LINES 1159, 1386–1388
Known stubs and maintenance hotspots
Some APIs are intentionally placeholders; a few implementation details deserve explicit review
STATIC EXPLANATION • SOURCE: g1/dev/sdk_wrapper_v3.py
35
Explicitly unimplemented
get_inspire_hand_sensors()
teach()
repeat()
They return a “hand not detected” result or raise NotImplementedError.
Do not treat the names as complete capabilities.
Hard-coded coupling
Joint count and index layout.
DDS topic names.
IP addresses and register addresses.
SLAM API IDs/version.
Piper model directory.
These are the first places to update for another robot/setup.
Review points
Broad except handling in hand APIs.
Private SDK _Call is used directly.
Wall-clock timestamps are not monotonic.
“latest” means newest callback, not synchronized sensor data.
get_state fans out across many possible failure points.

## Slide 36
QUICK INDEX
Method reference: startup, state, motion
Use this as a map back to the source file
STATIC EXPLANATION • SOURCE: g1/dev/sdk_wrapper_v3.py
36
Construction + state
517 G1.__init__
584 _load_type
599 _robot_state_client
612 _motion_client
620 _audio_client
628 _arm_action_client
642 _video_client
650 _slam_client
658 _lowcmd_client / _arm_sdk_client
725 get_state
738 get_service / toggle_service
790 mode setters
818 get_gait / toggle_gait
Telemetry + motion
859 get_lowstate
908 say
933 set_headlight
952 release_arms / engage_arms
1008 loco_move / loco_stop
1012 get_rgbd
1039 get_point_cloud
1064 get_slam_info
1079 move_ll_joint
1108 get_odom / get_imus
1150 get_battery

## Slide 37
QUICK INDEX
Method reference: hands, SLAM, audio, IK
The remaining public methods are grouped here by feature
STATIC EXPLANATION • SOURCE: g1/dev/sdk_wrapper_v3.py
37
Hands
1179 open_dex3_hand
1189 close_dex3_hand
1199 get_dex3_hand_sensors
1210 get_inspire_hand_sensors
1214 open_inspire_hand
1224 close_inspire_hand
SLAM + audio
1234 start_mapping
1239 stop_mapping
1243 relocate
1252 add_map_pose
1259 navigate
1275 get_mic_input
1296 clap / face_wave / high_wave
1309 shake_hand / hug / left_kiss
Arm geometry
1320 ik_move_ee
1371 extend_arm
1386 teach
1388 repeat
Private solver:
228 _solve_position_shoulder_elbow
Main write path:
436 _ArmSdk.write

## Slide 38
SUGGESTED READING ORDER
A safe way to approach this file
You can understand and test the wrapper incrementally
STATIC EXPLANATION • SOURCE: g1/dev/sdk_wrapper_v3.py
38
1
Read constants
joint IDs, topics, IPs
2
Run telemetry only
lowstate, odom, IMU, battery
3
Check services/modes
state without moving
4
Test outputs
audio, light, camera
5
Test hands
with physical clearance
6
Test motion/IK
simulation or lifted robot
Bottom line
sdk_wrapper_v3.py is a practical façade: it makes many robot capabilities callable from Python, but its correctness depends on the live Unitree SDK, network topology, message definitions, and physical safety setup.